Weekly Learning Journal

Due Sept. 13 midnight (Individual Effort): submit at MOST two (2) sentence summary for at least three (3) articles you read in the "Reading" section. Submit your summary through your Weekly Learning Journal.

Taking Temperature Measurements with RTDs: How-To Guide
Passing current through the RTD generates a voltage which allows you to measure the resistance of the material; the resistance changes linearly with temperature. Disadvantages of RTDs are their high costs, slow response time and being prone to heating themselves.

Measuring Temperature with an RTD or Thermistor
Thermistors are devices which measure temperature based on the changing resistance of a material with respect to temperature; unlike RTDs though, thermistors use metal oxide semiconductors as their measurement device. Thermistors are extremely sensitive instruments with fast response times, but have a very limited temperature range (because the semiconductor can melt).

Temperature Measurements with Thermistors: How-To Guide
Thermistors need an excitation source which will provide the device with a constant and precise current; this can be acomplished by connecting the two ends of the thermistor to the + and – ports of an analog channel on a DAQ. Though thermistors can be configured with 2, 3 or 4 wire configurations, a two wire one is the most common and simplest.