Prelab:
Read the datasheet of SN754410NE: http://www.ti.com/lit/ds/symlink/sn754410.pdf
Answer the following questions:

1. To which pins on SN754410NE will you connect the I/O ports of LM3S1968?
1,2EN: Pin 1 - Enable
1A: Pin 2 – Input to driver 1
2A: Pin 7 – Input to driver 2

2. To which ports can you connect the motors to? What is the maximum no. of motors that
can be connected to a SN754410NE?
The motors will be connected to the 1Y and 2Y pins on the SN754410NE

There are 4 seperate outputs on this chip, so we could connect 4 different motors.

3. What is the importance of VCC1 and VCC2? Do both the ports operate at same voltages?
They are not the same

VCC1 is the 5V supply for interal logic of the chip.

VCC2 is the power for the drivers, whatever we want to run the connected application at.

4. Draw a simple table listing all the possible outputs possible from SN754410NE’s output
port?

Its pretty one to one. The outputs of Y1 and Y2 can only be high if E1,2 is high. Same thing for Y2 and Y3 and E3,4. So excluding the enable inputs, we have this table

1A	2A	3A	4A	1Y	2Y	3Y	4Y
0	0	0	0	0	0	0	0
0	0	0	1	0	0	0	1
0	0	1	0	0	0	1	0
0	0	1	1	0	0	1	1
0	1	0	0	0	1	0	0
0	1	0	1	0	1	0	1
0	1	1	0	0	1	1	0
0	1	1	1	0	1	1	1
1	0	0	0	1	0	0	0
1	0	0	1	1	0	0	1
1	0	1	0	1	0	1	0
1	0	1	1	1	0	1	1
1	1	0	0	1	1	0	0
1	1	0	1	1	1	0	1
1	1	1	0	1	1	1	0
1	1	1	1	1	1	1	1

5. Come up with a block diagram of the experiment.