Name: James Kesley Richardson
ID: 1555520

Experiment 3 Thermistor and First Order Response

Exercise
Given the configuration shown in Figure 1, calculate the divider resistance R2 that will cause 27mW power dissipation by the Thermistor when Rth = 3k Ω.

Power Disipation = i^2 * Rth = 27mW

→ i = 3 * 10^-3
→ Vs = Rth + R2
→ Rth + R2 = 12 / (3 * 10^-3)
→ R2 = 1k Ω

Given the following resistance values output from thermistor

(1) is the temperature increasing or decreasing;
The temperature is increasing. Resistance decreases with temperature increases for a thermistor.

(2) calculate the corresponding temperature for each measurement
assume initial temperature is 20oC and the slope α =-10%/oC

We can use

R = Rref * (1 – α *ΔT ) -> Tf = {1 - { R } over { Rref }} over { α } + ti

t(s)	R(t)	Temperature
0	3500 	20oC
1	3400 	20.285oC
3	3300 	20.57oC
6	3200 	20.857oC
8	3100 	21.143oC
10	3060 	21.257oC
12	3000 	21.428oC

(3) calculate the time constant of the sensor using equation if the time constant of the thermistor is 10s

R(t) = Ri+ (Rf-Ri)[1 -e-t/τ]

 τ = {t} over {( ln(1 - {R(t) - Ri} over {Rf - Ri} ) )} = 10 over {( ln(1 - {3060 - 3500} over {3000 - 3500} ) )} = 6.21 seconds