Verilog and System Verilog

Primitives
The fundamental rules of Verilog primitives are that each instance must have exactly one output, unless the primitive is an inverter (NOT) or buffer (BUF). In those cases, each instance must have exactly one input but may have an arbitrary number of outputs.

Here is an instantiation of a 3 input NAND gate
nand #3 G1 (OUT, A, B, C)

Here, nand is a verilog keyword specifying the type of instance. #3 is the optional delay parameter. G1 is the name.

There are similar keywords for all of the boolean operations.

Chapter 3 – Behavioral Coding part 1
Top down design:
First steps are to design overall functionality, then the inputs and outputs. If you have this information, you can create the verilog module with the correct inputs and outputs and put off designing the behavior of the module until later.

Continuous assignments are considered the same was as gotos are in software programming… technically legal but frowned upon. Continuous assignments cause simulation to take longer because they have to reevaluate the assignment at every instant.

Functional Blocks
SystemVerilog adds extensions to always statements by allowing the always statement to clarify what type of hardware the block is to infer: combinational, latched, or registered. This is done by replacing the keyword “always” with always_comb, always_latch, or always_ff.

There are many added System Verilog features for verification, such as the fork...join block which will run all statements in parallel. A sensitivity list mixing edge-sensitive signals with other variables would fail at compile time. While simulators tend to allow mixed combinational and sequential sensitivity lists, synthesizers do not.

Synthesizers ignore combinational sensitivity lists. The list is only checked to determine if the logic generated should be combinational or sequential.

Since the 2001 language update, elements in sensitivity lists may be separated by either commas, as shown in Figure 3.4, or the word “or,” as shown in the last block of Figure 3.2.
always @(posedge CLK, negedge RST) begin

always @(posedge CLK or negedge RST) begin

Variables
There are two groups of variables, Nets and Registers.. kind of misnomers.
nets can have multiple drivers, which is the situation with Tri-state buses. It is not possible to make a Tri-state bus with nothing but register variables.

wire is a net, while reg is a register type. It is possible to go an entire career using nothing but these two variable types, but others can be useful. A few designers prefer to declare Tri-state nets as type “tri,” which work exactly as do variables of type wire. The point of using “tri” is simply to have the code self-document.

Verilog has a rigid rule on where net variables may be assigned values. They may never be assigned values inside of functional blocks (always or initial blocks). Their use is limited to being the target of continuous assignments and interconnects between instances of primitives or instantiated modules.

Any undeclared variables default to type single bit wire. There is a default_nettype directive that can change this. You can force all variables to be explicitly declared by saying
`default_nettype none
The “none” option is only suported in System Verilog.